Interior

Press Release
October 2008

The Key To Digital Tachograph Downloading 

The VDO Downloadkey second generation model brings more features to ensure downloading digital tachograph and driver data is quicker and easier for drivers and fleet operators.

To significantly reduce the time it takes to download digital tachograph data, the Downloadkey II features faster processors and is set to only download 'since last download' rather than the entire data.  The 16 times larger memory provides more capacity for approximately 1,500 bi-monthly downloads.  Other highlights include a traffic light indicator which clearly displays the download status and its memory capacity.  The key bears the traffic light system on both sides, where it is clearly visible to the driver, regardless of where the tachograph is mounted in the cab.  In addition, a bleeping sound occurs indicating the download is complete and the key should be removed.

"The VDO Downloadkey II is the ideal way for drivers and fleet operators to meet their legal requirement to download data from digital tachographs at least every 56 days and download the Driver Card at least every 28 days" says Peter Needham, VDO Product Manager.

The VDO Downloadkey II does not require a separate power supply and is compatible with all makes of digital tachograph.  The unit features a download plug which plugs directly into the digital tachograph, where it automatically downloads data from the unit.  At the opposite end is a USB high-speed plug which plugs directly into a computer and uploads data quickly and reliably.  Using the software included, the Downloadkey can be configured to download specific data such as detailed speed data, activities and technical faults. The data can also be imported for analysis into an analysis software package such as VDO TIS-Web.

The Download Starter Kit includes a VDO Downloadkey II, a user guide and box of 3 printer rolls and costs just £195 + VAT.  Free technical support is available and updates are provided via the VDO website.  Solutions are available to purchase on-line at www.vdoshop.co.uk or from our VOSA approved network of distributors.

About Continental

With annual sales of more than €25 billion (based on 2006 figures), the Continental Corporation is one of the top five automotive suppliers worldwide. As a supplier of brake systems, systems and components for the powertrain and chassis, instrumentation, infotainment solutions, vehicle electronics, tires and technical elastomers, the corporation contributes towards enhanced driving safety and protection of the global climate. Continental is also a competent partner in networked automobile communication. Today, the corporation employs approximately 150,000 people at nearly 200 locations in 36 countries.

Supplying both, OEMs and the Aftermarket worldwide, the Interior Division of Continental AG develops and produces electronic systems which allow the information in a vehicle to be controlled and communicated according to the requirements of the driver and the driving situation. The Division achieves annual sales of more then €6 billion with a workforce of more than 33,000 employees. The range of products includes instruments clusters and multifunctional displays, control units, electronic car entry systems, tire information systems, climate control systems, radios, multimedia and navigation systems, telematic solutions as well as cockpit modules and systems. The Interior Division develops vehicle electronics enabling car-to-car and car-to-infrastructure communication, Internet access and the seamless integration of mobile devices (car-to-device). The focus on systems integration offers customers less complexity and ensures efficient and cost-effective solutions for the management of information in passenger cars as well as commercial and special vehicles.

Lisa McCauley
Continental Automotive Trading UK Ltd
36 Gravelly Industrial Park, Birmingham B24 8TA
Tel: +44 (0)121 326 1162 / Fax: +44 (0) 121 326 1298
Email: uk@vdo.com
Web:  dtco.co.uk		                             
                                                                                                               A brand of the Continental Corporation